## Slide 1
Design of a Subsurface Robot Swarm
Embedded electronics, simulation and prototyping of Caiman robots fleet
Joab da Silva Bezerra
CNRS – Lab-STICC (UMR 6285) · ROBEX · ENSTA Brest · June to August 2026
Supervisors: Franck Ruffier (CNRS) · Quentin Brateau
Academic tutor: Prof. Philippe Xu
DEFENCE — 24 AUGUST 2026
Notes: [00:30 - cumulative 00:30]
Good morning. I am Joab da Silva Bezerra. This work was done at the Lab-STICC on the ENSTA Brest campus, in the ROBEX team, supervised by Franck Ruffier, with technical support from Quentin Brateau.
The presentation covers the Caiman board, its architecture and production file, a mission simulator, and a hardware-in-the-loop bench.
Move on at 30 seconds.

## Slide 2
THE SYSTEM
Caiman: vehicle and coverage budget
Bathymetric survey
Plume tracking
Structure inspection
Vehicle
Value
Pressure hull
PMMA cylinder
Battery
12 V / 56 A·h
Nominal energy
672 W·h
Propulsion
2 × T60
Motor draw (mean)
15 A / 180 W
Echosounder
Ping2, 25°
Depth sensor
Bar30
Surface radio
nRF24, 250 m
Ideal motors-only endurance 56 / 15 = 3.73 h. Modelling assumption, not a measured figure.
Why a fleet, in numbers
Single-beam footprint, h = 3 m, β = 25°:
d = 2h·tan(β/2)
1.33 m
Track length over the 0.32 km² polygon:
full cover: 0.32 km² / 1.33 m
240.6 km
recon grid: 0.32 km² / 26 m
12.3 km
19.5× fewer track-kilometres for the reconnaissance grid
Split across 5 vehicles: 2.46 km each, against 48.1 km each for full insonification. That ratio is what makes a fleet of cheap units the workable option.
Notes: [01:50 - cumulative 02:20]
What the object is, and the number that justifies the whole approach.
A Caiman is a small AUV for shallow-water survey: a sealed PMMA cylinder, a 12 volt 56 amp-hour Li-ion pack, so 672 watt-hours nominal, two T60 thrusters, a Bar30 depth sensor, a Ping2 echosounder and an nRF24 surface radio. Mean motor draw is 15 amps, 180 watts, which gives an ideal motors-only endurance of 3.73 hours. That is a modelling figure, not a measurement.
Now the coverage budget, on the right, because this is where the fleet argument actually comes from.
The Ping2 is a single-beam echosounder with a 25 degree cone. At 3 metres altitude the geometric footprint is 2 times 3 times the tangent of 12.5 degrees, so 1.33 metres.
The survey polygon is 0.32 square kilometres. If you wanted to insonify every square metre of it at that footprint, you need 0.32 square kilometres divided by 1.33 metres, which is 240.6 kilometres of track. At the reconnaissance grid spacing actually used, 26 metres, it is 12.3 kilometres.
That is a factor of 19.5. And split across five vehicles it is 2.46 kilometres each, against 48.1 kilometres each if one vehicle had to do the full job.
That ratio is the engineering reason for the fleet. It is also why the electronics have to be cheap: the approach only works if you can afford five of them.
IF ASKED about unit cost: I do not have a per-unit figure to give you. What I can state is the manufacturing envelope, which is on the routing slide: two layers, 116 placed components, 94.8 square centimetres.

## Slide 3
COMMUNICATION CONSTRAINT
No usable RF link in immersion
RF attenuation in seawater
Absorption over tens of centimetres rules out Wi-Fi and mesh networking.
Store-and-forward operation
Each vehicle buffers its survey to microSD and exchanges at surface contacts.
Link parameter
Value
Note
Surface range
250 m
nRF24, default profile
Raw rate
1 Mbit/s
physical layer
Packet loss
3 %
modelled
Telemetry period
5 s
per vehicle
Fleet offered load
256 bit/s
5 × 32 B / 5 s
Channel occupancy
0.026 %
of the 1 Mbit/s link
The radio is not the bottleneck: the fleet offers 256 bit/s against a 1 Mbit/s channel. The binding constraint is the surface window, not throughput.
AUV
Base
250 m
0.5 m
AUV
Below 0.5 m depth the adjacency is zero. Samples are timestamped and held on microSD until the next surface contact, then merged at the rendezvous.
Link condition applied in the simulator
Notes: [01:10 - cumulative 03:30]
Seawater absorbs electromagnetic waves within tens of centimetres, so Wi-Fi and the mesh networking used in aerial and ground swarms are unavailable. Acoustic modems propagate but are expensive, slow and power-hungry, which does not fit a low-cost fleet.
The operating mode that follows is store-and-forward: each vehicle buffers its survey to microSD and only exchanges when it surfaces.
Now the link budget, because it produces a result worth stating. The default profile is 250 metres range at 1 megabit per second, with 3 percent modelled packet loss and a 5 second telemetry period per vehicle. Five vehicles each sending 32 bytes every 5 seconds is 256 bits per second offered load.
Against a 1 megabit per second channel that is 0.026 percent occupancy. So the radio is nowhere near saturated. The binding constraint is not throughput, it is the surface window: how often a vehicle is above 0.5 metres and within 250 metres of a peer.
That is why the design effort went into the rendezvous logic and the frame format rather than into raw data rate.
The schematic on the right is the adjacency rule as applied in the simulator: above 0.5 metres a link exists, below it the adjacency is zero.

## Slide 4
SCOPE
Planned scope and delivered scope
Schematic and routing
Corrected, reviewed, production file generated
Production file
Gerbers, BOM, CPL — 5 boards ordered 23 June
Embedded software
Architecture and drivers on the target MCU
Swarm control
Deterministic simulator, five AUV
Protocol bench
ESP32 and Raspberry Pi, bidirectional
Tank and field trials
Outside the internship window
Notes: [00:40 - cumulative 04:10]
Where each item of the subject ended.
Delivered: the schematic and routing corrections, the production file, and the protocol bench on two processors. Partial: the embedded software, which has the architecture and the drivers for the target microcontroller, and swarm control, which exists as a deterministic simulator rather than on vehicles. Outside the window: tank and field trials.
Keep this short. Read the six labels and move to the architecture.

## Slide 5
ELECTRONICS
System architecture and interconnection
POWER
+BATT
12 V
→
LM74700
reverse / inrush
→
AP63205
5 V rail
→
AP63203
3.3 V rail
STM32F765VITx
Cortex-M7 at 216 MHz
STM32Cube and FreeRTOS
sensor task at 10 Hz
116 PARTS · 2 LAYERS · 94.8 CM²
I²C2 — inertial and environment
LSM6DSO accel/gyro · LIS2MDL
magnetometer · LPS22HB barometer
I²C1 — external connector
Bar30 depth and pressure sensor
SPI1 — radio
nRF24L01+ with CE, CSN and IRQ
SDMMC — storage
microSD with card-detect contact
UART — navigation aids
GNSS receiver · Ping2 echosounder
PWM — propulsion
Two ESC channels driving the T60 thrusters
GPIO — signalling
SK6812 RGB via SN74LV1T34 level shifter
ADC and GPIO — housekeeping
Battery · US1881 magnetic contact · leak
Buck converter
L
D
f_sw
ΔI_L
ΔI / I_out
I_pk at 2 A
I_sat
Margin
L1 — AP63205, 5 V
4.7 µH
0.42
1.1 MHz
0.56 A
28.2 %
2.28 A
2.5 A
8.7 %
L2 — AP63203, 3.3 V
3.3 µH
0.66
1.1 MHz
0.31 A
15.5 %
2.16 A
3.0 A
28.2 %
Notes: [02:00 - cumulative 06:10]
The board is organised around one microcontroller, an STM32F765VITx, Cortex-M7 at 216 megahertz, running STM32Cube and FreeRTOS with the sensor task at 10 hertz. 116 placed components on two layers, 94.8 square centimetres.
Power enters at the top. The 12 volt input is protected by an LM74700 ideal-diode controller against reverse polarity and inrush, then two cascaded synchronous bucks: an AP63205 for the 5 volt rail and an AP63203 deriving 3.3 volts from it.
The interfaces are grouped by function. On the left, two I2C buses, deliberately separated. I2C2 is the internal instrumentation bus carrying the LSM6DSO accelerometer and gyroscope, the LIS2MDL magnetometer and the LPS22HB barometer. I2C1 is brought out to a connector for the Bar30, which sits in the front end cap and therefore has to leave the board.
On the right, SPI1 for the nRF24 transceiver with its chip-enable, chip-select and interrupt lines; SDMMC for the microSD with card-detect, which is what makes store-and-forward possible; and a UART group for the GNSS receiver and the Ping2 echosounder.
At the bottom, two PWM channels for the ESCs driving the T60 thrusters, a GPIO line driving the SK6812 indicator through an SN74LV1T34 level shifter because the LED needs 5 volt logic, and an ADC and GPIO group for battery voltage, the US1881 Hall-effect contact and the leak detector. The magnetic contact exists because the hull is sealed: you cannot fit a switch.
Now the converter table at the bottom, which is the quantitative part.
Applying the standard buck relation, delta-I equals V-out times one minus D, over L times switching frequency. On L1 that gives 0.56 amps of ripple, which is 28.2 percent of the 2 amp rating. On L2, 0.31 amps, 15.5 percent. Both sit inside the usual 20 to 40 percent design band, L2 conservatively so.
Peak current is output plus half the ripple. L1 reaches 2.28 amps against a rated saturation of 2.5, so 8.7 percent margin. L2 reaches 2.16 against 3.0 amps, 28.2 percent margin. L1 is the tighter of the two and is the rail I would instrument first.

## Slide 6
EMBEDDED SOFTWARE
Firmware structure and task budget
Module group
Devices
State
Inertial and environment
LSM6DSO, LIS2MDL, LPS22HB
in main loop
Storage and housekeeping
microSD, battery ADC, RGB
in main loop
Radio, thrusters, depth
nRF24, ESC, Bar30
driver written
Navigation aids and safety
GNSS, Ping2, RC, leak, contact
skeleton
STM32Cube HAL with FreeRTOS. The application task initialises the sensor layer, then calls its service function on a 100 ms period, so a 10 Hz acquisition cadence against a 5 s telemetry period — fifty acquisition cycles per transmitted frame.
Timing budget
sensor task period
100 ms
acquisition rate
10 Hz
telemetry period
5 s
cycles per frame
50
Logger defect to correct: the CSV header declares ten columns while the application writes eighteen fields. It has to be reconciled before the logs are used quantitatively.
Notes: [01:00 - cumulative 07:10]
The firmware is STM32Cube HAL with FreeRTOS. The application task initialises the sensor layer and then calls its service function on a 100 millisecond period, so 10 hertz acquisition.
Put that against the 5 second telemetry period from the link budget and you get 50 acquisition cycles per transmitted frame. Which is the reason the frame carries a compacted snapshot rather than a sample stream: at 10 hertz you cannot transmit every sample through a surface-only link, so the vehicle logs locally and sends state.
By module group: the inertial and environment sensors and the storage and housekeeping group are called from the main loop. The radio, the ESCs and the Bar30 have drivers written but sit outside the audited application path. The navigation aids and the safety inputs are skeletons.
One defect I will state because it affects data quality: the CSV logger declares ten columns in its header and writes eighteen fields. That has to be reconciled before the logs are used quantitatively.

## Slide 7
ELECTRONICS REVIEW
Schematic corrections on the inherited design
Decoupling placed in series
C12–C18 sat in series on V_DD, V_DDA and V_BAT instead of in parallel to ground.
A series capacitor is an open circuit at DC: the 3.3 V rail did not reach pins 11, 27, 50, 75, 100 and 71.
Commit
Correction
Effect
dd041de
C12–C18 returned to parallel, rail to GND
DC continuity
c66b3fb
LSM6DSO ground pin electrical type
matrix conflict cleared
2be6335
Redundant power flags removed
net declarations clean
10 → 0 blocking ERC errors, KiCad 10.0.5 (42 minor warnings remain)
BEFORE
AFTER
Series on the rail, then parallel to ground
Notes: [01:15 - cumulative 08:25]
The corrections applied to the inherited schematic.
The significant one: the 100 nanofarad decoupling capacitors on VDD, VDDA and VBAT were drawn in series on the supply rails rather than in parallel to ground. A capacitor in series is an open circuit at DC, so the 3.3 volt rail did not reach pins 11, 27, 50, 75, 100 and 71.
Commit dd041de returns C12 to C18 to parallel between the rail and ground, restoring DC continuity while keeping the high-frequency decoupling the reference manual specifies.
Two further corrections in the table: c66b3fb fixes the electrical type of the LSM6DSO ground pin, which was producing a conflict in the KiCad interconnection matrix, and 2be6335 removes redundant power flags.
The measurable outcome is blocking ERC errors going from ten to zero under KiCad 10.0.5. Forty-two minor warnings remain and are listed in the report.

## Slide 8
ROUTING
Design rules and manufacturing margins
Constraint
Project rule
Process capability
Margin
Internal copper clearance
0.150 mm
0.100 mm
+50 %
Minimum track width
0.127 mm
0.100 mm
+27 %
Minimum via diameter
0.300 mm
0.200 mm
+50 %
Rules were set from the published tolerance grid and then tightened, so the layout keeps margin against the process floor rather than sitting on it.
Documented exclusion
Measured
Against capability
U5 — /I2C2_SCL to GND
0.1291 mm
+29 % above 0.100 mm
U8 — INT2 pad
0.1472 mm
+47 % above 0.100 mm
U2 — BST / SW pins
0.1320 mm
vendor footprint, fixed
U6 — unconnected pad
—
no electrical function
Every deviation sits above the published process capability and is recorded in the project file with its justification, rather than removed by relaxing the rule set globally.
100.87 × 93.94 mm · 2 layers · 1 oz · ENIG · IPC class 2
Notes: [01:10 - cumulative 09:35]
The design rules and the margin they leave.
The top table: the project rules were taken from the manufacturer's published tolerance grid and then tightened. Internal copper clearance 0.150 millimetres against a 0.100 capability, so 50 percent margin. Minimum track 0.127 against 0.100, 27 percent. Minimum via 0.300 against 0.200, 50 percent. The layout therefore keeps margin rather than sitting on the process floor.
The second table lists the four deviations that were accepted, with their measured values. The largest, U5, is 0.1291 millimetres between I2C2_SCL and ground inside the package, which is below my own 0.150 rule but 29 percent above the 0.100 millimetre capability. U8's INT2 pad is 0.1472, so 47 percent above capability. U2's BST and SW pins are set by the manufacturer's footprint and cannot be changed. U6 is an unconnected pad with no electrical function.
The point is that each of these sits above what the process can actually hold, and each is recorded in the project file with its justification. They were not removed by lowering the rule set globally, which would have hidden them.
The board is 100.87 by 93.94 millimetres, two layers, 1 ounce copper, ENIG finish, IPC class 2, flying-probe tested.

## Slide 9
DESIGN FOR MANUFACTURABILITY
Power inductor selection
Board pads in green against the candidate terminations in red
The PCBA engineering review flagged that the pre-selected inductor terminations exceeded the drawn land pattern. Selection was redone against pad geometry as a first-order constraint.
Designator
Value
Part
LCSC
I_sat
Footprint
L1 — 5 V buck
4.7 µH
Würth 74438356047
C2045367
2.5 A
WE-MAPI 4020
L2 — 3.3 V buck
3.3 µH
Würth 74438356033
C2045382
3.0 A
WE-MAPI 4020
L2 moves from the schematic value of 3.9 µH to 3.3 µH. Ripple rises from 0.26 A to 0.31 A, about 18 %, and the peak stays at 72 % of saturation — the substitution costs nothing in margin.
Identical 4 × 4 mm package outlines carried incompatible pad geometry. Selection is constrained by the land pattern before it is constrained by the value.
Notes: [01:00 - cumulative 10:35]
The power inductor selection, which was redone during PCBA preparation.
The manufacturer's engineering review flagged that the terminations of the pre-selected parts exceeded the land pattern drawn on the board. You can see the overhang in the image: board pads in green, candidate terminations in red.
The selection was redone with pad geometry as a first-order constraint rather than an afterthought, and checked against inductance, rated thermal current, saturation current and DC resistance. The result is the table: both positions on the WE-MAPI 4020 footprint, L1 at 4.7 microhenry with 2.5 amps saturation, L2 at 3.3 microhenry with 3.0 amps.
L2 moves from the schematic value of 3.9 microhenry to 3.3. That raises its ripple from 0.26 to 0.31 amps, about 18 percent, and the peak stays at 72 percent of saturation. So the substitution costs nothing in margin.
The general point is on the dark card: two components with identical 4 by 4 millimetre package outlines had incompatible pad geometry. Component selection is constrained by the land pattern before it is constrained by the electrical value.

## Slide 10
METHOD
Validating the fleet layer before the hardware arrives
Board fabrication and assembly run on their own lead time. The fleet behaviour, the protocol and its security properties do not depend on that board, so they were specified, implemented and exercised in parallel.
Simulator
Fleet logic, rendezvous, faults
→
Protocol
32-byte frame, AEAD, anti-replay
→
HIL bench
Same C source, two processors
Notes: [00:55 - cumulative 11:30]
This slide states the working method for the second half of the internship.
Board fabrication and assembly run on their own lead time. But the fleet layer does not depend on that board: the mission logic, the rendezvous behaviour, the frame format and its security properties are all specifiable and testable independently.
So they were developed in parallel, in three steps. A deterministic simulator for the fleet logic, the rendezvous and the fault scenarios. A protocol specified to the physical constraint of the radio, with authenticated encryption and anti-replay. And then a hardware-in-the-loop bench running that same C source on two physical processors.
The three next slides follow that order.

## Slide 11
SIMULATION
Deterministic mission model
Mission view after the first rendezvous
Parameter
Value
Vehicles
5
Compute zone
1000 × 700 m
Survey polygon
0.32 km²
Bottom depth
13–20 m
Survey altitude
3 m
Beam width
25°
Footprint
1.33 m
Grid spacing
26 m
Track length
12.3 km
A fixed seed reproduces terrain, mission decisions and packet outcomes, so two runs differ only where a parameter was deliberately changed.
The station displays received telemetry only. Delayed samples are replayed from their timestamps rather than interpolated on arrival.
Notes: [01:40 - cumulative 13:10]
The simulator is a system-level model, not a hydrodynamic one. Its purpose is the fleet layer: mission distribution, the rendezvous, the link condition and the fault scenarios.
The parameter table on the right is the reference configuration and it ties back to the coverage budget from the second slide. Five vehicles over a thousand by seven hundred metre zone, a 0.32 square kilometre survey polygon, synthetic bottom between 13 and 20 metres. Vehicles fly boustrophedon transects at 3 metres altitude with the 25 degree beam, giving the 1.33 metre footprint, on a 26 metre grid, for the 12.3 kilometres of track we computed earlier.
Determinism: a fixed seed reproduces the terrain, the mission decisions and the packet outcomes. Two runs differ only where a parameter was deliberately changed, which is what makes a comparison between configurations meaningful.
And the design point I would highlight, on the amber card: the supervision view shows received telemetry only. After a dive the station holds the last position received by radio and propagates the commanded route with growing uncertainty; it does not read the model's internal state. When delayed telemetry arrives at a rendezvous the samples are replayed from their timestamps rather than interpolated, so the reconstructed track is the one actually flown.
That separation is what makes the supervision view a usable operator tool rather than a display of ground truth.

## Slide 12
DEMONSTRATION
Supervision interface
RUN LIVE — 60 S
SEVEN SUPERVISION VIEWS
Mission
Robots
Network
Commands
Security
Packet Log
Events
Python 3.12 and Streamlit containerised behind a Caddy reverse proxy with a health endpoint. Run here from a local instance.
Notes: [01:00 - cumulative 14:10] << HARD CAP: 60 SECONDS.
>>> LIVE. Started before the call opens. Do not launch it here.
SETUP BEFORE THE CALL
cd simulator && streamlit run app.py
Browser at http://localhost:8501, window sized for share, default seed, five AUV.
Advance the clock just past the first rendezvous so the grid is partly synchronised.
Deck on a second display.
SEQUENCE - four steps, about 15 seconds each. Do not explore.
1. Mission view. State that this shows received telemetry only. Point at one last-known marker.
2. Advance the clock. Submerged vehicles stop updating: the adjacency rule, live.
3. Network view at a rendezvous. Edges appear; trace the multi-hop route to the base.
4. Security view. Tamper the AEAD tag once and show the rejection counter increment by category.
Then stop. Do not open Packet Log or Events unless asked.
IF IT FAILS: 15 seconds maximum, then move to the backup slide.
Say once: containerised behind a Caddy reverse proxy with a health endpoint, deployed to a VPS
under the caimansim.fr domain; running here from a local instance.

## Slide 13
BACKUP
Interface captures
Rendezvous: four AUV surfaced, active links, multi-hop route to base
Capture scenario: R1 taken, key 1 compromised, renewal pending
Capture scenario. The compromised vehicle's key is revoked. Submerged peers receive no immediate recall: they continue to their next surface contact, take the authenticated return order there, and are rekeyed with the captured node excluded. The group key keeps the demonstration legible; a production system needs per-vehicle roots and pairwise traffic keys.
Notes: [Skip unless the live instance failed. Budget 0:00.]
Left: network view at a rendezvous. Right: the physical capture scenario.
On the capture case: the key of the captured vehicle is revoked. The submerged peers receive no immediate recall, because there is no link to them. They continue to their next surface contact, take the authenticated return order there, and are rekeyed with the captured node excluded.
The group key keeps the demonstration legible. A production system needs per-vehicle roots and pairwise traffic keys.
Then continue to the frame format.

## Slide 14
PROTOCOL
Frame format and link budget
8 B
header
8 B
encrypted payload
16 B
Poly1305 tag
one tick per byte · 32 B is the nRF24 physical payload limit
Quantity
Value
Derivation
Application efficiency
25 %
8 B of 32 B
Max fragments
16
4-bit index
Max logical payload
128 B
16 × 8 B
Frame air time
256 µs
256 bit at 1 Mbit/s
With PHY overhead
320 µs
+8 B preamble, addr, CRC
The 8 encrypted bytes carry x/y position, vehicle depth, bottom depth, battery, link quality, leak flag and GNSS availability, packed into 64 bits.
Cryptographic construction
256-bit per-mission master key; HKDF-SHA-256 derives separate encryption, routing and fingerprint material.
ChaCha20-Poly1305 AEAD — no AES accelerator on this MCU.
Monotonic per-source sequence in the nonce, anti-replay window, relay de-duplication cache.
Relays retransmit the 32 bytes unchanged: TTL and hop count stay in local policy, ciphertext and tag are never rewritten.
Notes: [01:35 - cumulative 15:45]
The nRF24 has a fixed 32-byte physical payload, so the frame was specified to that limit rather than around it.
The allocation is eight bytes of header, eight bytes of encrypted payload and sixteen bytes of Poly1305 tag. Into those 64 payload bits go x and y position, vehicle depth, bottom depth, battery, link quality, a leak flag and GNSS availability.
The table gives the derived quantities. Application efficiency is 25 percent, eight useful bytes in thirty-two. The fragment index is four bits, so sixteen fragments maximum, which bounds the logical payload at 128 bytes. Frame air time is 256 bits at 1 megabit per second, so 256 microseconds; adding the nRF24 preamble, address and CRC takes it to about 320.
Put that against the link budget from earlier: 256 microseconds of air time every 5 seconds per vehicle is why fleet occupancy came out at 0.026 percent.
On the crypto: a 256-bit per-mission master key, with HKDF-SHA-256 deriving separate material for encryption, routing and the displayed fingerprint. ChaCha20-Poly1305 for the AEAD, chosen because this microcontroller has no AES accelerator and ChaCha is efficient and constant-time in software. A monotonic per-source sequence goes into the nonce, with an anti-replay window and a de-duplication cache at relays.
And relays retransmit the 32 bytes unchanged: TTL and hop count are local policy, the ciphertext and its tag are never rewritten.
IF ASKED about 25 percent: truncating the tag trades forgery resistance for payload, and authenticating a fragment group rather than each fragment would amortise it. The full tag was chosen because the objective was the security property, not throughput — and at 0.026 percent occupancy there is no throughput pressure to trade against.

## Slide 15
HARDWARE-IN-THE-LOOP
Protocol running on two processors
16 August 2026: ESP32 as R1, Raspberry Pi 4 as R2
Node
Hardware
Toolchain
R1
ESP32-D0WDQ6
ESP-IDF 6.0.2
R2
Raspberry Pi 4B
GCC 14.2.0, Mbed TLS 3.6.5
Cycle
R1 → R2 seq
R2 → R1 seq
ACK
1
102762
32769
TX_DS
2
102763
32770
TX_DS
3
102764
32771
TX_DS
4
102765
32772
TX_DS
5
102766
32773
TX_DS
Sequence numbers strictly increasing on both nodes, which is the condition the anti-replay window relies on. Every frame 32 B, authenticated and decoded at the far end.
Transport on this bench is Wi-Fi/UDP over an access point raised by the ESP32; the nRF24 FIFO, interrupt and retransmission behaviour is modelled in software.
Notes: [01:45 - cumulative 17:30]
The protocol implementation running on physical processors.
Two nodes. An ESP32-D0WDQ6 as vehicle R1, firmware built with ESP-IDF 6.0.2 and flashed over a CP210x serial link. A Raspberry Pi 4 Model B as R2, with the native executables rebuilt on the Pi itself using GCC 14.2 and Mbed TLS 3.6.5. The same portable C source compiles for both.
The second table is the actual run from 16 August: five complete bidirectional cycles. R1 sends sequences 102762 through 102766, R2 answers with 32769 through 32773, and each transmission is acknowledged by the nRF24 model with a TX_DS.
What matters in that table is not the count but the monotonicity: sequence numbers strictly increasing on both nodes is exactly the condition the anti-replay window relies on. Every frame is 32 bytes, authenticated and decoded at the far end.
A detail worth mentioning: a sixth transmission from R1 ended in MAX_RT because R2 had exited after the five requested cycles. That is the missing-acknowledgement path being exercised, unintentionally but usefully.
The scope of the bench, on the card at the bottom: the transport is Wi-Fi and UDP over an access point raised by the ESP32, and the nRF24 FIFO, interrupt and retransmission behaviour is modelled in software. So what the bench establishes is the protocol, the cryptographic operations and the bidirectional scheduling on real silicon.

## Slide 16
SCHEDULE
Three months, and the bring-up sequence
June
STM32/IMU bench
Schematic and PCB corrected
Production file, order 23rd
July
Fleet simulator
Web supervision
Capture scenario
August
HIL on two processors
Inductor re-selection
Report
Bring-up sequence on delivery
Continuity on +3V3 / GND before any power is applied
Current-limited ramp, measure both rails under load
Instrument the 5 V rail current — L1 has the tighter margin
Flash the STM32, bring peripherals up one bus at a time
Notes: [01:00 - cumulative 18:30]
The distribution of the three months.
June: the exploratory STM32 and inertial bench, the schematic and PCB corrections, the production file and the order on the 23rd. July: the fleet simulator, the web supervision interface and the capture scenario. August: the HIL on two processors, the inductor re-selection after the PCBA review, and the report.
What carries beyond the internship: the simulator and its test suite specify the expected fleet behaviour independently of any particular board, so they serve as a reference for the final firmware. The protocol implementation is portable C already running on two processors. And the HIL bench remains valid when the Wi-Fi transport is replaced by the nRF24 link.
The bring-up sequence is the order I would follow. Continuity on the 3.3 volt and ground rails before any power is applied. Then a current-limited ramp with both rails measured under load. Then instrument the 5 volt rail current specifically, because L1 is the tighter margin at 8.7 percent. Then flash the STM32 and bring peripherals up one bus at a time.
One procedural point I am keeping: design rules, justified exclusions and the exported production files are versioned alongside the schematic, so the order is reproducible from the repository.

## Slide 17
SUMMARY
A manufacturable production file for a fleet-capable AUV board,
a deterministic mission model, and a portable protocol
running authenticated on two processors.
94.8
cm², 2 layers
116
components
672
W·h nominal
12.3
km survey track
32
B authenticated frame
Thank you. I am available for questions.
Joab da Silva Bezerra · CNRS – Lab-STICC · ROBEX · 24 August 2026
Notes: [00:30 - cumulative 19:00]
To summarise. The internship produced a manufacturable production file for a board capable of operating in a fleet, a deterministic mission model that specifies the fleet behaviour, and a portable protocol implementation running authenticated exchanges on two processors.
The figures on the strip are the ones that characterise the work: a 94.8 square centimetre two-layer board with 116 components, 672 watt-hours of nominal energy, 12.3 kilometres of survey track for the reference mission, and a 32-byte authenticated frame.
Thank you. I am available for questions.
Then stop talking.